## Slide 1: APSSDC EMBEDDED SYSTEM ADVANCED WORKSHOP (IoT with Raspberry Pi)

## Slide 2: Arduino & Raspberry Pi

## Slide 3: The Arduino Development Board
Making-robots-with-arduino.pdf

## Slide 4: Raspberry Pi

## Slide 5: What is Raspberry Pi
The Raspberry Pi is a low cost, credit-card sized computer that plugs into a computer monitor or TV, and uses a standard keyboard and mouse.
The Raspberry Pi was created in Febuary 2012 by the Raspberry Pi Foundation
Official site: www.raspberrypi.org

## Slide 6: Arduino VS Raspberry Pi
 | Arduino | Raspberry Pi
Clock Speed | 16 MHz | >700 MHz
Processor | 8 Bit | 64 Bit
Operating system | Not Support | Support Operating system
Programming | Either C/C++ | Support Diff. Programming language’s
Internet | Need to use External Hardware | Easily Connected

## Slide 7: Raspberry Pi Models
Raspberry Pi 3 Model B
Raspberry Pi 2 Model B
Raspberry Pi 1 Model B+
Raspberry Pi 1 Model B
Raspberry Pi 1 Model A
Raspberry Pi 1 Model A+
Raspberry Pi Zero W
Raspberry Pi Zero

## Slide 8: Raspberry Pi Models
Raspberry Pi 1 model B+ Raspberry Pi Zero Raspberry Pi 3 Model B

## Slide 9: Raspberry Pi 3 Model B

## Slide 10: Raspberry Pi 3 Model B
BCM43438 WiFi/BT chip

## Slide 11: Specifications
SoC: Broadcom BCM2837
CPU: 4× ARM Cortex-A53, 1.2GHz
GPU: Broadcom Video Core IV
RAM: 1GB LPDDR2 (900 MHz)
Networking: 10/100 Ethernet, 2.4GHz 802.11n wireless
Bluetooth: Bluetooth 4.1 Classic, Bluetooth Low Energy Storage: microSD
GPIO: 40-pin header
Ports: HDMI, 3.5mm analogue audio-video jack, 4× USB 2.0, Ethernet, Camera Serial Interface (CSI), Display Serial Interface (DSI)

## Slide 12: Raspberry Pi Networking

## Slide 13: Raspberry Pi Networking-Via Ethernet

## Slide 14: Raspberry Pi Networking-Via WiFi
Raspberry Pi-3 Built in WiFi

## Slide 15: DSI(Display Serial Interface) Port
The Raspberry Pi connector S2 is a display serial interface (DSI) for connecting a liquid crystal display (LCD) panel using a 15-pin ribbon cable.
The mobile industry processor interface (MIPI) inside the Broadcom BCM2837 IC feeds graphics data directly to the display panel through this connector

## Slide 16: CSI(Camera Serial Interface) Port
The Raspberry Pi has a Mobile Industry Processor Interface (MIPI) Camera Serial Interface Type 2 (CSI-2), which facilitates the connection of a small camera to the main Broadcom BCM2835 processor

## Slide 17: GPIO Pins

## Slide 18: Equipment Needed to set up Raspberry Pi

## Slide 19: Equipment Needed..
A Monitor with VGA/HDMI cable
Power supply
USB Keyboard and Mouse
SD Card

## Slide 20: Setup..

## Slide 21: Hardware Setup..

## Slide 22: Software setup..
Select the Operating System
Download the Operating system
Format SD card
Burn(Flash) the SD card

## Slide 23: Operating system
NOOBS
Raspbian
Raspberry Pi Desktop
Thirty Party operating system-Ubuntu Mate
-Windows IoT core
-PINET
                -RISC OS

## Slide 24: NOOBS(New Out of Box Software)
Operating systems included in NOOBS are
Raspbian
Pidora
LibreELEC
OSMC
RISC OS
Arch Linux

## Slide 25: Format SD card…
Sdcard.org->Download SD card formatter
Install the software

## Slide 26: NOOBS(New Out of Box Software)
NOOBS—NOOBS
-NOOBS LITE

## Slide 27: RASPBIAN
RASPBIAN STRETCH WITH DESKTOP
RASPBIAN STRETCH LITE

## Slide 28: BURN(FLASH) O.S
ETCHER-Software(etcher.io)